## Slide 1: Module 1 : Introduction to Internet
Internet Communication Engineering

## Slide 2: What is Internet
A network of networks, joining many government, university and private computers together.
Provides an infrastructure for the use of E-mail, bulletin boards, file archives etc other computational resources.
The vast collection of computer networks which form and act as a single huge network for transport of data and messages across distances .
The largest network of networks in the world.
Uses TCP/IP protocols and packet switching .
Runs on any communications substrate.

## Slide 3
Interconnection of Networks: Internet
A heterogeneous network made of four WANs and two LANs

## Slide 4
Hierarchical organization of the Internet

## Slide 5: Evolution of Internet
1970 ARPANET(Advanced Research Projects Agency) - 15 nodes
1972 first email
1982 TCP/IP becomes internet standard
  Transmission Control Protocol/Internet Protocol
1984 ARPANET - 1,000 nodes
1986 NSF(National Science Foundation)-Net backbone on ARPANET
1987 ARPANET - 10,000 nodes

## Slide 6: Contd…
1988 - businesses begin to connect to system for research purposes
1989 ARPANET - 100,000 nodes
1989 link email between CompuServe and ARPANET
1990 ARPANET becomes the Internet

## Slide 7: Internet History

## Slide 8: A Brief Summary of the Evolution of the Internet
1945
1995
Memex
Conceived
1945
WWW
Created
1989
Mosaic
Created
1993
A
Mathematical
Theory of
Communication
1948
Packet
Switching
Invented
1964
Silicon
Chip
1958
First Vast
Computer
Network
Envisioned
1962
ARPANET
1969
TCP/IP
Created
1972
Internet
Named
and
Goes
TCP/IP
1984
Hypertext
Invented
1965
Age of
eCommerce
Begins
1995

## Slide 9: From Simple, But Significant Ideas Bigger Ones Grow 1940s to 1969
1945
1969
We can access
information using
electronic computers
We do it reliably with “bits”,
sending and receiving data
We can do it cheaply by using
Digital circuits etched in silicon.
We can accomplish a lot by having a
vast network of computers to use for
accessing information and exchanging ideas
We will prove that packet switching
works over a WAN.
Packet switching can be used to
send digitized data though
computer networks
Hypertext can be used to allow
rapid access to text data

## Slide 10: From Simple, But Significant Ideas Bigger Ones Grow 1970s to 1995
1970
1995
Ideas from
1940s to 1969
We need a protocol for Efficient
and Reliable transmission of
Packets over a WAN: TCP/IP
The ARPANET needs to convert to
a standard protocol and be renamed to
The Internet
Computers connected via the Internet can be used
more easily if hypertext links are enabled using HTML
and URLs: it’s called World Wide Web
The World Wide Web is easier to use if we have a browser that
To browser web pages, running in a graphical user interface context.
Great efficiencies can be accomplished if we use
The Internet and the World Wide Web to conduct business.

## Slide 11: The creation of Internet
The creation of the Internet solved the following challenges:
  Basically inventing digital networking as we know it
  Survivability of an infrastructure to send / receive high-speed electronic messages
  Reliability of computer messaging

## Slide 12: Protocols and Standards
protocols and standards.
Protocol is synonymous with rule.
Standards are agreed-upon rules.
Protocols
Syntax → format of the data
Semantics → meaning of each section
Timing → when data should be sent and how fast.
Standards
De facto → by fact (not approved as a standard)
De jure → by Law (approved)

## Slide 13: Protocols and Standards
Standards Organizations
International Organization for Standardization (ISO)
International Telecommunication Union - Telecommunication Standards (ITU-T)
American National Standards Institute (ANSI)
Institute of Electrical and Electronics Engineers (IEEE)
Electronic Industries Association (EIA)

## Slide 14: There are 2 standard Network Models : - OSI Model - TCP/IP Protocol Suite
Network Models

## Slide 15: Layered Tasks
A network model is a layered architecture
  Task broken into subtasks
  Implemented separately in layers in stack
  Functions need in both systems
  Peer layers communicate
Protocol:
  A set of rules that governs data communication
  It represents an agreement between the communicating devices

## Slide 16: Tasks involved in sending a letter

## Slide 17
Seven layers of the OSI model
OSI Layered Architecture
Layers
Layer 7. Application
Layer 6. Presentation
Layer 5. Session
Layer 4. Transport
Layer 3. Network
Layer 2. Data Link
Layer 1. Physical
Sender
Receiver

## Slide 18: Layered Architecture
A layered model
Each layer performs a subset of the required communication functions
Each layer relies on the next lower layer to perform more primitive functions
Each layer provides services to the next higher layer
Changes in one layer should not require changes in other layers
The processes on each machine at a given layer are called peer-to-peer process

## Slide 19: Peer to peer process
Communication must move downward through the layers on the sending device, over the communication channel, and upward to the receiving device
Each layer in the sending device adds its own information to the message it receives from the layer just above it and passes the whole package to the layer just below it
At the receiving device, the message is unwrapped layer by layer, with each process receiving and removing the data meant for it

## Slide 20: Contd…
The passing of the data and network information down through the layers of the sending device and backup through the layers of the receiving device is made possible by interface between each pair of adjacent layers
Interface defines what information and services a layer must provide for the layer above it.

## Slide 21: Physical Layer
The physical layer is responsible for movements of
individual bits from one hop (node) to the next.
Function
  Physical characteristics of interfaces and media
  Representation of bits
  Data rate
  Synchronization of bits
  Line configuration (point-to-point or multipoint)
  Physical topology (mesh, star, ring or bus)
  Transmission mode ( simplex, half-duplex or duplex)

## Slide 22
Physical layer

## Slide 23: Network Layer
The network layer is responsible for the delivery of individual packets from
the source host to the destination host.
Source-to-destination delivery
Responsible from the delivery of packets from the original source to the final destination
Functions
  Logical addressing
  routing

## Slide 24: Network Layer

## Slide 25: Transport Layer
The transport layer is responsible for the delivery of a message from one process to another.
Process-to- process delivery
Functions
  Port addressing
  Segmentation and reassembly
  Connection control ( Connection-oriented or connection-less)
  Flow control
  Error control

## Slide 26: Transport Layer
Segmentation and reassembly

## Slide 27: Session Layer
The session layer is responsible for dialog control and synchronization.
  It establishes, maintains and synchronize the interaction between communicating system
  Function
    Dialog control
    Synchronization (checkpoints)

## Slide 28
Synchronization
Session layer

## Slide 29
Presentation Layer
The presentation layer is responsible for translation, compression, and encryption.
  Concerned with the syntax and semantics of the information exchanged between two system
  Functions
    Translation ( EBCDIC-coded text file  ASCII-coded file)
    Encryption and Decryption
    Compression

## Slide 30
Presentation layer

## Slide 31
Application Layer
The application layer is responsible for providing services to the user.
Functions
  Network virtual terminal (Remote log-in)
  File transfer and access
  Mail services
  Directory services (Distributed Database)
  Accessing the World Wide Web

## Slide 32: Application Layer

## Slide 33: Summary of Layers

## Slide 34: TCP/IP Protocol Suite
The layers in the TCP/IP protocol suite do not exactly match those in the OSI model. The original TCP/IP protocol suite was defined as having four layers: host-to-network, internet, transport, and application. However, when TCP/IP is compared to OSI, we can say that the TCP/IP protocol suite is made of five layers: physical, data link, network, transport, and application.

## Slide 35: TCP/IP and OSI model

## Slide 36
Internet Layer
TCP/IP support the Internet Protocol IP ( unreliable).
IP is a host-to-host protocol.
Supporting protocols:
Address Resolution Protocol (ARP)
Reverse Address Resolution Protocol (RARP)
Internet Control Massage Protocol (ICMP)
Internet Group Massage Protocol (IGMP)

## Slide 37
Transport Layer
Process-to-process protocol.
User Datagram Protocol (UDP)
Transmission Control Protocol (TCP)
Stream Control Transmission Protocol (SCTP)

## Slide 38
ADDRESSING
Four levels of addresses are used in an internet employing the TCP/IP protocols: physical, logical, port, and specific.

## Slide 39
Relationship of layers and addresses in TCP/IP

## Slide 40
Physical Address
Physical addresses are imprinted on the NIC. Most local-area networks (Ethernet) use a 48-bit (6-byte) physical address written as 12 hexadecimal digits; every byte (2 hexadecimal digits) is separated by a colon.
Example:
07:01:02:01:2C:4B A 6-byte (12 hexadecimal digits) physical address.

## Slide 41
Physical Address
known also as the MAC address
Is the address of a node as defined by its LAN or WAN
It is included in the frame used by data link layer
The physical addresses in the datagram may change from hop to hop.

## Slide 42
Port addresses
Port address is a 16-bit address represented by one decimal number ranged from (0-65535) to choose a process among multiple processes on the destination host.
Destination port number is needed for delivery.
Source port number is needed for receiving a reply as an acknowledgments.
In TCP/IP , a 16-bit port address represented as one single number. Example: 753
The physical addresses change from hop to hop,
but the logical and port addresses usually remain the same.

## Slide 43
Logical Address
IP addresses are necessary for universal communications that are independent of physical network.
No two host address on the internet can have the same IP address
IP addresses in the Internet are 32-bit address that uniquely define a host.
The physical addresses will change from hop to hop,
but the logical addresses usually remain the same.

## Slide 44
Specific addresses
E-mail address (user1@ksu.edu.sa)
Universal Resource Locator (URL) (www.ksu.edu.sa)
The Domain Name System (DNS) translates human-friendly computer hostnames ( URL) into IP addresses. For example, www.example.com is translated to 208.77.188.166

## Slide 46: Advantages of TCP/IP
It helps you to establish/set up a connection between different types of computers.
It operates independently of the operating system.
It supports many routing-protocols.
It enables the internetworking between the organizations.
TCP/IP model has a highly scalable client-server architecture.

## Slide 47: Functions

## Slide 48: Contd…

## Slide 49: Contd…

## Slide 50: Contd…