## Slide 1: Internet Communication Engineering
Module 4 : Multimedia Communications

## Slide 2: Multimedia Communications
Introduction :
The term multimedia is used to indicate that the information/ data being transferred over the network.
The information may be composed of one or more of the following media types :-
Text : includes unformatted and formatted text.
Unformatted text : Comprising strings of characters from a limited character set.
Formatted text : Comprising strings as used for the structuring, access and presentation of electronic documents.
1

## Slide 3: Multimedia Communications
Images : Include computer generated images comprising lines, curves and circles and digitized images of documents and pictures.
Audio : Includes both low fidelity speech (as used in telephony) and high fidelity stereophonic music (as used with compact discs.
Video: Includes short sequences of moving images.
3

## Slide 4: Multimedia Information Representation
Text and Images : Applications involving text and images comprise blocks of digital data.
In case of text, a typical unit is a block of characters with each character represented by a fixed number of bits known as codeword.
A digitized image comprises a two dimensional block of picture elements with each element represented by a fixed number of bits.
4

## Slide 5: Multimedia Information Representation
Audio & Video: Applications involving audio and video uses analog signal.
Audio & video signals vary continuously with time as the amplitude of the speech, audio and video signal varies.
The duration of applications that involve audio and/or video can be relatively long.
In case of text and image, standard form of representation is digital form.
But in case of audio & video form, because their basic forms of representation are analog signals, these must be converted into a corresponding digital form.
5

## Slide 6: Digitization Principle
Analog Signals : The general properties relating to any time varying analog signal shown in fig., the amplitude of such signals varies continuously with time.
In addition, a mathematical technique known as Fourier analysis can be used to show that any time varying analog signal is made up of a possibly infinite number of single frequency sinusoidal signals whose amplitude and phase vary continuously with time relative to each other.
6

## Slide 7
7

## Slide 8: Digitization
The range of frequencies of the sinusoidal components that make up a signal is called the signal bandwidth.

## Slide 9: Digitizing Audio & Video
Digitizing Audio :
When sound is fed into a microphone, an electronic analog signal is generated that represents the sound amplitude as a function of time.
This signal is called analog audio signal.
This analog signal can be digitized to produce a digital signal.
Voice is sampled at 8000 samples/sec with 8 bits/ sample. This results in digital signal of 64 kbps. Music is sampled at 44100/sec with 16 bits/sample. Results in digital signal of 705.6 kbps for monaural and 1.411 Mbps for stereo.

## Slide 10: Digitizing Audio & Video
Digitizing Video :
A video consists of a sequence of frames.
If the frames are displayed on the screen fast enough, we get an impression of motion. The reason is our eyes cannot distinguish the rapidly flashing frames as individual ones.
Each frame is divided into small grids called picture elements or pixels.
For black and white TV, each 8 bit pixel represents one of the 256 different gray levels. For color TV, each pixel is 24 bits, with 8 bits for each primary color.

## Slide 11: Compression
Data compression is the art or science of representing information in a compact form. We create these compact representations by identifying and using structures that exist in the data.
Data compression is important to storage systems because it allows more bytes to be packed into a given storage medium than when the data is uncompressed.
Compression also reduces file transfer time, saving time and communications bandwidth.
11

## Slide 12: Audio & Video Compression
12
To send audio or video over the Internet requires Compression.
Audio Compression :
Audio compression can be used for speech or music.
For speech, we need to compress 64 khz digitized signal & for music, we need to compress 1.411 Mhz signal.
Two Types : Predictive & Perceptual Encoding

## Slide 13: Predictive Encoding
Differences between the samples are encoded instead of encoding all the sampled values.
Several standards are defined : GSM, G.729 and G.723.3.

## Slide 14: Perceptual Encoding: MP3
Most common compression technique used to create CD quality audio is based on perceptual encoding.
MP3 (MPEG Audio layer 3) uses this technique.
Based on the science of psychoacoustics (study of how people perceive sound).
Frequency Masking : Loud sound in a frequency range can partially or totally mask softer sound in another frequency range.
Temporal Masking : A loud sound can numb our ears for a short time even after the sound has stopped.

## Slide 15: Contd…
MP3 uses these two phenomena to compress Audio signals.
The technique analyses and divides the spectrum into several groups.
Zero bits are allocated to the frequency ranges that are allocated to the frequency ranges that are totally masked
A small no. of bits are allocated to the frequency range that are partially masked.
A large no. of bits are allocated to the freq range that are not masked.
MP3 produces 3 data rates : 96 kbps, 128 kbps and 160 kbps.

## Slide 16: Video Compression
Video is composed of multiple frames.
Image is made up of frames.
We can compress video by first compressing images.
There are two standards used for compression
: JPEG(used for image compression) & MPEG (used for video compression).

## Slide 17: Image Compression : JPEG
In JPEG, a gray scale picture is divided into blocks of 8x8 pixels.

## Slide 18: JPEG
The purpose of dividing the picture into blocks is to decrease the number of calculations because the no. of mathematical operations for each picture is the square of the number of units.
The whole idea of JPEG is to change the picture into a linear set of numbers that reveals the redundancies.
And the redundancies can then be removed by using one of the text compression methods.

## Slide 19: JPEG Process

## Slide 20: JPEG Process
Discrete Cosine Transform (DCT) :
In this step, each block of 64 pixels goes through a transformation called DCT.
The transformation changes the 64 values so that the relative relationships between pixels are kept but the redundancies are revealed.

## Slide 21: 3 Cases
Case 1 :
We have a block of uniform gray and the value of each pixel is 20.
When we do the transformations, we get a nonzero value for the first element, the rest of the pixels have a value of 0.

## Slide 22
Case 1
Uniform Gray Scale

## Slide 23: Case 2
Two Sections:
In this case, we have a block with two different uniform gray scale sections.
There is a sharp change in the values of the pixels from 20 to 50.
When we do transformations, we get DC value as well as nonzero AC values

## Slide 24: Case 3
Gradient Gray Scale:
In this case, we have a block that changes gradually.
That is , there is no sharp change between the values of neighbouring pixels.
When we do transformations, we get DC value with many nonzero AC values also.

## Slide 25: Quantization
After T table is created, the values are quantized to reduce the number of bits needed for encoding.
We divide the number by a constant and then drop the fraction.
This reduces the required number of bits.

## Slide 26: Compression
After quantization, the values are read from the table, and redundant 0s are removed.
However, to cluster the 0s together, the table is read diagonally in a zigzag fashion rather than row by row or column by column.
The reason is that if the picture changes smoothly, the bottom right corner of the table is all 0s.

## Slide 28: Video Compression: MPEG
The MPEG method is used to compress video.
In principle, a motion picture is a rapid flow of a set of frames, where each frame is an image.
In other words, a frame is a spatial combination of pixels and a video is a temporal combination of frames that are sent one after another.
- Compressing video means spatially compressing each frame and temporally compressing a set of frames.

## Slide 29: Spatial Compression
The spatial compression of each frame is done with JPEG.
Each frame is a picture that can be independently compressed.

## Slide 30: Temporal Compression
In temporal compression, redundant frames are removed.
When we watch television, we receive 50 frames/sec.
However, most of the consecutive frames are almost the same.
For ex when someone is talking, most of the frame is the same as the previous one except for the segment of the frame around the lips which changes from one frame to another.

## Slide 31: Temporal Compression
MPEG-2 takes high correlation that exists between successive pictures of a video to compress a series of moving images.
To temporally compress data, the MPEG method first divides frames into 3 categories: I frames, P- frames and B-frames.
I(Intra picture),P(predicted picture),B(Bidirectional predicted picture)

## Slide 32
Contd…
In MPEG , every Mth picture in a sequence can be fully compressed by using a standard MPEG algorithm, these are I frames.
Then successive I frames are compared and the portion of the image that have moved are identified.
The image sections which do not move are carried forward in time domain to intermediate pictures by the decoder memory.
Then a subset of intermediate pictures is selected and the prediction and correction of locations of the image section which have moved is carried out.

## Slide 33: Contd…
These predicted and corrected images are the P- pictures.
The pictures between I and P pictures are the B pictures. They incorporate the stationary image sections uncovered by the moving sections.

## Slide 34
I Frames
Intercoded frame is an independent frame that is not related to any other frame.
They are present at regular intervals.
It must appear periodically to handle some sudden change in the frame that the previous and following frames cannot show.
I-frames are independent of other frames and cannot be constructed from other frames.

## Slide 35
P Frames
Predicted frame is related to the preceding I-frame or P frame.
In other words, each P-frame contains only the changes from the preceding frame.
The changes, however cannot cover a big segment.
These frames can be constructed only from previous I or P frames.
These frames carry much less information than other frame types and carry even fewer bits after compression.
Bidirectional frame is related to preceding and following I frame or P frame.

## Slide 36
B Frames
Bidirectional frame is related to preceding and following I frame or P frame.
In other words, each B-frame is relative to the past and the future.
B-frame is never related to another B-frame.

## Slide 37: MPEG frame construction

## Slide 38
Compression Process
The I frames are compressed as if they are JPEG images.
The compressed images are then applied to four 8x8 blocks called macro blocks.
The macro blocks are down sampled for subsequent compression of chrominance component.

## Slide 39: Contd…
The first step in MPEG is to identify the macroblocks moved between the I frames.
Next step is to form the P frames between the I frames.
The difference between the predicted and true position of the macro block represents the error in prediction.
This error is then compressed using DCT and used for correcting the P frame.

## Slide 40: MPEG-4
- MPEG-4 is a standard used for defining the compression of audio and visual digital data.
- The MPEG-2
standard does not support
multimedia. Therefore MPEG-4 standard was developed.
The MPEG-4 file is created by tracking the individual objects within a scene separately and compressing them together.
MPEG-4 is optimized for low as well as very high bit rates
Using MPEG-4 the users can control objects in a scene independently. Thus, MPEG-4 introduces interactivity.

## Slide 41: MPEG-4 Functions
To improve coding efficiency.
To encode mixed media data including
video,
audio or speech.
To enable robust transmission by reducing errors.
To enable the user to interact with the audio visual scene.
To multiplex and synchronize data associated with media objects to ensure their efficient transport over the network channels.
Interaction with the AV scene which is formed on the receiver side.

## Slide 42: Profiles and Levels
- MPEG-4 provides a large and rich set of tools for encoding.
For specific applications subsets of MPEG-4 tool sets have been provided for users’ convenience.
These subsets are called as profiles. Each profile is further divided into multiple levels. This reduces the computational complexity.
A combination of profile and levels should be used according to the needs of an application.

## Slide 43: ITU Standards
- ITU-T stands for Telecommunication standardization sector of ITU.
- The primary function of ITU-T efficient and timely production
is to ensure the of standards that
cover all the fields in telecommunication worldwide.
The international standards produced by ITU-T are called as Recommendation. They become mandatory only when they are adopted as a part of national law.
Some of the important standards published by ITU-T are as follows :
Audio compression & coding : G.711, G.722, G.723, G.726, G.728, G.729
Video compression & coding : H.261,H.262,H.263,H.264,H.265

## Slide 44: H.261 Standard
H.261 is an ITU-T DCT based video compression standard.
It is the first member of the H.26X family of video
video
coding standards in the domain of ITU-T coding Experts Group (VCEG).
This standard assumes one of two formats : CIF and QCIF

## Slide 45: Specifications

## Slide 46: Design Details

## Slide 47: H.261 Block Diagram
Loop filter
Motion compensation Motion estimation Quantizer
Frame memory

## Slide 48: Contd…
An input image is divided into blocks of 8x8 pixels.
For a given 8x8 block, we subtract the prediction generated using the previous frame.
The difference between the block being encoded and the prediction is transformed using a DCT.
The transform coefficients are quantized and the quantization label encoded using a variable length code.

## Slide 49: Motion Compensation

## Slide 50: Performance

## Slide 51: H.261 Vs MPEG

## Slide 52: H.261 Decoder

## Slide 53: H.262 Standard
H.262 is also known as MPEG-2 video standard which was developed and maintained jointly by ITU-T & MPEG.
Also provides support for the interlaced video used in NTSC(National Television Standards Committee), PAL(Phase Alternate Line) and SECAM(Sequential Color & Memory) systems.
It supports very wide range of applications from mobile to HD editing

## Slide 54: H.262 Standard
Therefore for many applications it is not practical to support the entire standard.
Such applications are allowed to support only subsets of nth entire standard which are called as profiles and levels.

## Slide 55: H.263 Standard
H.263 is a video compression standard which was originally designed to operate as a low bit rate format for the video conferencing
Later, it was also used in the systems based on H.323 and H.320 such as RTP/IP video conferencing or ISDN based video conferencing.
Also used in the systems based on RTSP(Real Time Streaming Protocol) & SIP(Session Initiation Protocol ) .

## Slide 56: H.264 / MPEG-4
H.264 is typically used for lossy video compression even though the amount of loss is very small.
It is also possible to create a completely lossless compression using H.264.
It can be used for a very broad range of applications supporting very low to very high bit rates.

## Slide 57: H.323
H.323 is a standard designed by ITU in order to make the voice communication between the telephones on the public telephone network with the computers connected to the Internet .
Internet is connected to the telephone network via a gateway.
Gateway is a 5 layer device which makes the communication between one protocol stack to another possible by translating the messages.

## Slide 59: Operation
Terminal sends broadcast message to the gatekeeper. Gatekeeper in response sends its IP address.
The terminal communicates with gatekeeper. They negotiate with the help of H.225 protocol.
The terminal, gatekeeper, gateway and telephone communicate with each other with the help of H.245 and negotiate the compression method to be used.

## Slide 60: Contd…
The terminal, gatekeeper, telephone exchange the audio information with the help of RTP under the management of RTCP.
The termination of connection can be exercised by the terminal, gatekeeper, gateway and the telephone communicating with each other using Q.931 protocol.

## Slide 61: Streaming live audio/video
It is similar to the broadcasting of audio and video by radio and TV stations.
Instead of broadcasting to the air, the stations broadcast through the Internet.
There are several similarities between streaming stored audio/video and streaming live audio/video. They are both sensitive to delay; neither can accept retransmission.
However, there is a difference. In the first application, the communication is unicast and on- demand. In the second, the communication is multicast and live.

## Slide 62: Real-time interactive audio/video
In real-time interactive audio/video, people communicate with one another in real time.
The Internet phone or voice over IP is an example of this type of application.
Video allows orally.
that
conferencing is another example people to communicate visually and

## Slide 63: Characteristics
Time Relationship :
- Real time data on a packet switched network require preservation of the time relationship between packets of a session.

## Slide 64: Time Relationship

## Slide 65: Timestamp

## Slide 66
Jitter
Jitter is introduced in real time data by the delay between packets.

## Slide 67
Playback Buffer
In order to separate arrival time from the playback time,buffer is required to store the data until they are played back.This buffer is playback buffer.

## Slide 68: Other Characteristics
Ordering : A sequence number on each packet is required for real time traffic.
Multicasting : The traffic can be heavy therefore can be distributed using multicasting methods.
Translation : Meaning is changing the encoding of a payload to a lower quality to match the bandwidth of the receiving network.
Mixing : Mixing means combining several streams of traffic into one stream.

## Slide 69: Support from Transport Layer Protocol
TCP, with all its sophistication, is not suitable for interactive multimedia traffic because we cannot allow retransmission of packets.
UDP is more suitable than TCP for interactive traffic. However, we need the services of RTP, another transport layer protocol, to make up for the deficiencies of UDP.

## Slide 70: RTP
Real Time Transport Protocol (RTP) is designed to handle real time traffic on the Internet.
The main contributions of RTP are timestamping , Sequencing and mixing facilities.
Position of RTP in protocol suit

## Slide 71: RTP Packet Format

## Slide 72: Contd…
Ver : 2-bit field defines version number. Current version is 2.
P : 1 bit field set to 1 indicates presence of padding at the end of the packet. Padding is the norm if a packet is encrypted.If P=0 there is no padding.
X : 1 bit field set to 1 indicates extra extension header between basic header and the data.
Contributor Count : 4 bit field indicates number of contributors.(at most 14 contributers)

## Slide 73: Contd…
M : 1 bit Marker field used by the application to indicate end of its data.
Payload type : 7 bit field indicates type of the payload.

## Slide 74: Contd…
Sequence Number : 16 bit field used to number RTP packets. The sequence number of first packet is chosen randomly and it is incremented by 1 for each subsequent packet.
Timestamp : 32 bit field indicates time relationship between the packets. The timestamp for the first packet is a random number, for each succeeding packet the value is the sum of preceding timestamp plus the time the first byte is produced.

## Slide 75: Contd…
Synchronization source identifier : 32 bit field defines the source. If there are several sources then mixer is the synchronization source and other sources are contributors.
Contributor identifier : Each of these 32 bit identifiers defines a source.

## Slide 76: RTCP
RTP allows only one type of message, one that carries data from the source to the destination.
In many cases, there is a need for other messages in a session.
These messages control the flow and quality of data and allow the recipient to send feedback to the source or sources.
Real-Time (RTCP) is a purpose.
Transport protocol
Control Protocol designed for this

## Slide 77: RTCP Message Types

## Slide 78: Contd…
Sender report:Include timestamp information.
Receiver report:Informs the sender and other receivers about the QoS.
Source Description Message : The source periodically sends a source description message to give additional information about itself. This information can be name, email address, telephone number and address of the owner or controller of the source.
Bye Message : A source sends a bye message to shut sown a stream.
Application Specific Message : is a packet for an application that wants to use new applications. It allows the definition of a new message type.

## Slide 79: VoIP
One more real-time interactive audio/video application: voice over IP, or Internet telephony.
The idea is to use the Internet as a telephone network with some additional capabilities.
Instead of communicating over a circuit- switched network, this application allows communication between two parties over the packet-switched Internet.
Two protocols have been designed to handle this type of communication: SIP and H.323.

## Slide 80: SIP
Session Initiated Protocol (SIP) is an application layer protocol that establishes, manages and terminates a multimedia session.
It can be used to create two party, multiparty or multicast sessions.
SIP can run on either UDP, TCP or SCTP.

## Slide 81: Messages
SIP is a text based protocol like HTTP.
Hence like HTTP it uses messages.
6 messages are defined.

## Slide 82: Contd…
The caller initializes a session with the INVITE message.
After the callee answers the call, the caller sends an ACK message for confirmation.
The BYE message terminates the session.
The OPTION message queries a machine about its capabilities.
The CANCEL message cancels an already started initialization process.
The REGISTER message makes a connection when the callee is not available.

## Slide 83: SIP Formats
In SIP, email address, IP address, telephone number and other types of addresses can be used to identify the sender and receiver.
However, the address needs to be in SIP format.

## Slide 84: Simple Session
A simple session using SIP consists of 3 modules : Establishing, Communicating and Terminating.
Following is the simple session using SIP.

## Slide 85: Contd…
1. Establishing a session : Establishing a session in SIP requires a 3 way handshake.
The caller sends an INVITE message using UDP, TCP or SCTP to begin the communication.
If the callee is willing to start the session, will send a reply message.
To confirm that a reply code has been received, the caller sends an ACK message.

## Slide 86: Contd…
Communicating : After the session has been established, the caller and the callee can communicate using two temporary ports.
Terminating the session: The session can be terminated with a BYE message sent by either party.

## Slide 87: Tracking the Callee
SIP has a mechanism that finds the IP address of the terminal at which the callee is sitting.
To perform this tracking, SIP uses the concept of registration.
SIP defines some servers as registrars. At any moment a user is registered with at least one registrar server & this server knows the IP address of the callee.

## Slide 88: Contd…

## Slide 89: H.323 Protocols