## Slide 1: Chapter 6 RTL Design (Ref- Frank Wahid ch-5) EXTC – TE – DVLSI Swati Rane Assistant Professor Dept. of Electronics and Telecommunication SIES Graduate School of Technology
DVLSI

## Slide 2: RTL Design- Introduction
Processors:
  Programmable
  Custom designed (non-programmable)
Custom Processor: perform a particular task using
  Controllers
    Control input/output: single bit (or just a few) representing event or state
    Finite-state machine describes behavior; implemented as state register and combinational logic
  Datapath components
    Data input/output: Multiple bits collectively representing single entity
    Datapath components included registers, adders, ALU, comparators, register files, etc.

## Slide 3
    Register-transfer level (RTL) is a design abstraction which models a custom processor (synchronous digital circuit) in terms of
      the flow of digital signals (data) between hardware registers, and
      the logical operations performed on those signals.
    RTL Design:
  Specifies the registers of a design
  Describes the possible transfers and operations performed on input, output and register data
  Defines the control that specifies when to transfer and operate on data.

## Slide 4: RTL design
Review
  Combinational Logic Design
    First step: Capture behavior (using equation or truth table)
    Remaining steps: Convert to circuit
  Sequential Logic Design
    First step: Capture behavior (using FSM)
    Remaining steps: Convert to circuit
RTL design
  First step: Capture behavior (using high level state machine).
  Remaining steps: Convert to circuit.

## Slide 5: RTL Design Process

## Slide 6: High Level State Machines
FSM is not sufficient for capturing the data aspects of the system behavior
FSM consists of inputs, outputs(limited to Boolean types), states, state actions (limited to Boolean equations), state transition (limited to Boolean expressions)
High level state machines can be used to capture more complex logic involving multi-bit variables
High Level State Machines (HLSM) extend FSMs with features that make it possible to capture more complex behaviors.
  Multi-bit data inputs and outputs
    Assumed unsigned unless specified as signed
  Local storage
    Registers loaded on rising clock edges (i.e. when leaving a state)
  Arithmetic operations
    Add, Multiply, Compare, Bit Shift, etc

## Slide 7: HLSM Conventions
All inputs, outputs and local storage are defined at the top of the HLSM diagram
  Bit lengths are included in this definition
  All outputs are registered.
  Local storage values are always registered.
Registered values change on rising clock edges (i.e. when leaving a state)
Transition bits are implicitly ANDed with rising clock edge
Any unregistered output not explicitly assigned is 0.
Any registered value not explicitly assigned holds it’s value.

## Slide 8: Soda dispenser Machine
c: bit input, 1 when coin deposited.
a: 8-bit input having value of deposited coin.
s: 8-bit input having cost of a soda.
d: bit output, processor sets to 1 when total value of deposited coins equals or exceeds cost of a soda.

## Slide 9: Step 1-Capture High Level FSM

## Slide 10: Step2- Create Data Path

## Slide 11: Step 3-Create Data path to controller

## Slide 12: Derive Controllers FSM

## Slide 13: Completing Design

## Slide 14: Final Implementation

## Slide 15: RTL Designs categories
Control-dominated design
Data-dominated design

## Slide 16: Data Dominated RTL Design Example: FIR Filter